## Slide 1: 8085 MICROPROCESSOR PROGRAMS

## Slide 2: Store 8-bit data 52 H in memory Location 4000H

## Slide 3: Method 1
Program 1:
MVI A, 52H : "Store 52H in the accumulator"
STA 4000H : "Copy accumulator to 4000H"
HLT : "Terminate program execution"

## Slide 4: Method 2
Program 2:
LXI H : "Load HL with 4000H"
MVI M : "Store 32H in memory location
pointed by HL register pair
(4000H)"
HLT : "Terminate program execution"

## Slide 5: Exchange the contents of memory locations 2000H and 4000H.

## Slide 6: Method 1
Program 1:
LDA 2000H : "Get the contents of ML 2000H to A
MOV B, A : "Save the contents into B register"
LDA 4000H : "Get the contents of ML 4000H to A
STA 2000H : "Store the contents of A to ML 2000H"
MOV A, B : "Get the saved contents back into A
STA 4000H : "Store A to address 4000H"

## Slide 7: Method 2
Program 2:
LXI H 2000H : Initialize HL register pair as a pointer to ML
2000H."
LXI D 4000H : "Initialize DE register pair as a pointer to memory
location 4000H."
MOV B, M : "Get the contents of memory location 2000H into B register."
LDAX D : "Get the contents of memory location 4000H into A register."
MOV M, A : "Store the contents of A register into memory location
2000H."
MOV A, B : "Copy the contents of B register into accumulator."
STAX D : "Store the contents of A register into memory location 4000H."
HLT : "Terminate program execution."

## Slide 8
Add the contents of memory locations 4000H and 4001H and place the result in memory location 4002H.Sample problem
(4000H) = 14H
(4001H) = 89H
Result = 14H + 89H = 9DH

## Slide 9
Source program
LXI H 4000H : "HL points 4000H"
MOV A, M : "Get first operand"
INX H : "HL points 4001H"
ADD M : "Add second operand"
INX H : "HL points 4002H"
MOV M, A : "Store result at 4002H"
HLT : "Terminate program execution"

## Slide 10: Add two 16-bit numbers
Source Program 1:
LHLD 4000H : "Get first I6-bit number in HL"
XCHG : "Save first I6-bit number in DE"
LHLD 4002H : "Get second I6-bit number in HL"
MOV A, E : "Get lower byte of the first number"
ADD L : "Add lower byte of the second number"
MOV L, A : "Store result in L register"
MOV A, D : "Get higher byte of the first number"
ADC H : "Add higher byte of the second number with CARRY"
MOV H, A : "Store result in H register"
SHLD 4004H : "Store I6-bit result in memory locations 4004H and 4005H"
HLT : "Terminate program execution"

## Slide 11
Source program 2:
LHLD 4000H : Get first I6-bit number
XCHG : Save first I6-bit number in DE
LHLD 4002H : Get second I6-bit number in HL
DAD D : Add DE and HL
SHLD 4004H : Store I6-bit result in memory locations 4004H and 4005H.
HLT : Terminate program execution

## Slide 12
Add the contents of memory locations 40001H and 4001H and place the result in the memory locations 4002Hand 4003H.
(4000H) = 7FH
(400lH) = 89H
Result = 7FH + 89H = lO8H
(4002H) = 08H
(4003H) = 0lH

## Slide 13
program:
LXI H, 4000H : "HL Points 4000H"
MOV A, M : "Get first operand"
INX H : "HL Points 4001H"
ADD M : "Add second operand"
INX H : "HL Points 4002H"
MOV M, A : "Store the lower byte of result at 4002H"
MVIA, 00 : "Initialize higher byte result with 00H"
ADC A : "Add carry in the high byte result"
INX H : "HL Points 4003H"
MOV M, A : "Store the higher byte of result at 4003H"
HLT : "Terminate program execution"

## Slide 14
Find the l’s complement of the number stored at memory location 4400H and store the complemented number at me
mory location 4300H.
Sample problem:
(4400H) = 55H
Result = (4300B) = AAB

## Slide 15
LDA 4400B : "Get the number"
CMA : "Complement number"
STA 4300H : "Store the result"
HLT : "Terminate program execution"

## Slide 16
Find the 2′s complement of the number stored at memory location 4200H and store the complemented number at memory location 4300HSample problem:
(4200H) = 55H
Result = (4300H) = AAH + 1 = ABH

## Slide 17
Source program:
LDA 4200H : "Get the number"
CMA : "Complement the number"
ADI, 01 H : "Add one in the number"
STA 4300H : "Store the result"
HLT : "Terminate program execution"

## Slide 18
Search the given byte in the list of 50 numbers stored in the consecutive memory locations and store the address of memory location having the matched byte in the memory locations 2200H and 2201H. Assume byte is in the C register and starting address of the list is 2000H. If byte is not found store 00 at 2200H and 2201H.

## Slide 19
LX I H, 2000H :"Initialize memory pointer 50H“ HL= 2000
MVI B, 50H :"Initialize counter"
BACK: MOV A, M :"Get the number"
CMP C :"Compare with the given byte"
JZ LAST :"Go last if match occurs"
INX H :"Increment memory pointer“ HL=2001
DCR B :"Decrement counter“ 49=B
JNZ BACK :"If not zero, repeat"
LXI H, 0000H
SHLD 2200H
JMP END :"Store 00 at 2200H and 2201H"
LAST: SHLD 2200H :"Store memory address“ 2200=L,2201=H
END: HLT :"Stop"

## Slide 20
Calculate the sum of series of even numbers
Calculate the sum of series of even numbers from the list of numbers. The length of the list is in memory location 2200H and the series itself begins from memory location 2201H. Assume the sum to be 8 bit number so you can ignore carries and store the sum at memory location 2210H.Sample problem 2200H= 4H 2201H= 20H 2202H= l5H 2203H= l3H 2204H= 22H Result 22l0H= 20 + 22 = 42H = 42H

## Slide 21
LDA 2200H
MOV C, A :"Initialize counter"
MVI B, 00H :"sum = 0"
LXI H, 2201H :"Initialize pointer"
BACK: MOV A, M :"Get the number"
ANI 0lH :"Mask Bit l to Bit7"
JNZ SKIP :"Don’t add if number is ODD"
MOV A, B :"Get the sum"
ADD M :"SUM = SUM + data"
MOV B, A :"Store result in B register"
SKIP: INX H :"increment pointer"
DCR C :"Decrement counter"
JNZ BACK :"if counter 0 repeat"
STA 2210H :"store sum"
HLT

## Slide 22: ADDITION OF TWO 8 BIT NUMBERS
AIM: To perform addition of two 8 bit numbers using 8085.
ALGORITHM:
Start the program by loading the first data into Accumulator.
MVI A,DATA 1
Move the data to a register (B register).
MOV B,A
Get the second data and load into Accumulator.
MVI A,DATA 2
Add the two register contents. ADDB
Check for carry.
Store the value of sum and carry in memory location.
Terminate the program.

## Slide 23
Input: | 80 (4150)
 | 80 (4251)
Output: | 00 (4152)
 | 01 (4153)

## Slide 24
MVI | C, 00 | Initialize C register to 00
LDA | 4150 | Load the value to Accumulator.
MOV | B, A | Move the content of Accumulator to B register.
LDA | 4151 | Load the value to Accumulator.
ADD | B | Add the value of register B to A
JNC | LOOP | Jump on no carry.
INR | C | Increment value of register C
LOOP: STA | 4152 | Store the value of Accumulator (SUM).
MOV | A, C | Move content of register C to Acc.
STA | 4153 | Store the value of Accumulator (CARRY)
HLT |  | Halt the program.
PROGRAM:

## Slide 25
Source program:
LXI H, 4000H : "HL Points 4000H"
MOV A, M : "Get first operand"
INX H : "HL Points 4001H"
ADD M : "Add second operand"
INX H : "HL Points 4002H"
MOV M, A : "Store the lower byte of result at 4002H"
MVIA, 00 : "Initialize higher byte result with 00H"
ADC A : "Add carry in the high byte result"
INX H : "HL Points 4003H"
MOV M, A : "Store the higher byte of result at 4003H"
HLT : "Terminate program execution"

## Slide 26
Find the square of the given numbers from memory location 6100H and store the result from memory location 7000H.Sample problem 2200H = 4H 2201H= 9AH 2202H= 52H 2203H= 89H 2204H= 3FH Result = 89H + 3FH = C8H 2300H= H Lower byte 2301H = H Higher byte

## Slide 27
LXI H, 6200H :"Initialize lookup table pointer"
LXI D, 6100H :"Initialize source memory pointer"
LXI B, 7000H :"Initialize destination memory pointer"
BACK: LDAX D :"Get the number"
MOV L, A :"A point to the square"
MOV A, M :"Get the square"
STAX B :"Store the result at destination memory location"
INX D :"Increment source memory pointer"
INX B :"Increment destination memory pointer"
MOV A, C
CPI 05H :"Check for last number"
JNZ BACK :"If not repeat"
HLT