## Slide 1: 8085 MICROPROCESSOR PROGRAMS

## Slide 2: Add two 16-bit numbers
Source Program 1:
LHLD 4000H : "Get first I6-bit number in HL"
XCHG : "Save first I6-bit number in DE"
LHLD 4002H : "Get second I6-bit number in HL"
MOV A, E : "Get lower byte of the first number"
ADD L : "Add lower byte of the second number"
MOV L, A : "Store result in L register"
MOV A, D : "Get higher byte of the first number"
ADC H : "Add higher byte of the second number with CARRY"
MOV H, A : "Store result in H register"
SHLD 4004H : "Store I6-bit result in memory locations 4004H and 4005H"
HLT : "Terminate program execution"

## Slide 3
Source program 2:
LHLD 4000H : Get first I6-bit number
XCHG : Save first I6-bit number in DE
LHLD 4002H : Get second I6-bit number in HL
DAD D : Add DE and HL
SHLD 4004H : Store I6-bit result in memory locations 4004H and 4005H.
HLT : Terminate program execution

## Slide 4
Find the 2′s complement of the number stored at memory location 4200H and store the complemented number at memory location 4300HSample problem:
(4200H) = 55H
Result = (4300H) = AAH + 1 = ABH

## Slide 5
Source program:
LDA 4200H : "Get the number"
CMA : "Complement the number"
ADI, 01 H : "Add one in the number"
STA 4300H : "Store the result"
HLT : "Terminate program execution"

## Slide 6
Search the given byte in the list of 50 numbers stored in the consecutive memory locations and store the address of memory location in the memory locations 2200H and 2201H. Assume byte is in the C register and starting address of the list is 2000H. If byte is not found store 00 at 2200H and 2201H.

## Slide 7
LX I H, 2000H :"Initialize memory pointer 52H"
MVI B, 52H :"Initialize counter"
BACK: MOV A, M :"Get the number"
CMP C :"Compare with the given byte"
JZ LAST :"Go last if match occurs"
INX H :"Increment memory pointer"
DCR B :"Decrement counter"
JNZ B : Back "If not zero, repeat"
LXI H, 0000H
SHLD 2200H
JMP END :"Store 00 at 2200H and 2201H"
LAST: SHLD 2200H :"Store memory address"
END: HLT :"Stop"

## Slide 8
Calculate the sum of series of even numbers
Calculate the sum of series of even numbers from the list of numbers. The length of the list is in memory location 2200H and the series itself begins from memory location 2201H. Assume the sum to be 8 bit number so you can ignore carries and store the sum at memory location 2210H.
Sample problem 2200H= 4H ,2201H= 20H 2202H= l5H ,2203H= l3H ,2204H= 22H Result 22l0H= 20 + 22 = 42H = 42H

## Slide 9
LDA 2200H
MOV C, A :"Initialize counter"
MVI B, 00H :"sum = 0"
LXI H, 2201H :"Initialize pointer"
BACK: MOV A, M :"Get the number"
ANI 0lH :"Mask Bit l to Bit7"
JNZ SKIP :"Don’t add if number is ODD"
MOV A, B :"Get the sum"
ADD M :"SUM = SUM + data"
MOV B, A :"Store result in B register"
SKIP: INX H :"increment pointer"
DCR C :"Decrement counter"
JNZ BACK :"if counter 0 repeat"
STA 2210H :"store sum"
HLT