## Slide 1: Program
Add the contents of memory locations 4000H and 4001H and place the result in memory location 4002H.Sample problem
(4000H) = 14H
(4001H) = 89H
Result = 14H + 89H = 9DH

## Slide 2
Source program
LXI H 4000H : "HL points 4000H"
MOV A, M : "Get first operand"
INX H : "HL points 4001H"
ADD M : "Add second operand"
INX H : "HL points 4002H"
MOV M, A : "Store result at 4002H"
HLT : "Terminate program execution"

## Slide 3
3. Add two 8-bit numbers
Example
(2501 H) = 99H
(2502 H) = 39H
Result (2503 H) = 99H + 39H = D2H
Since,
1 0 0 1 1 0 0 1 (99H)
+ 0 0 1 1 1 0 0 1 (39H)
1 1 0 1 0 0 1 0 (D2H)

## Slide 4
4.Program
LXI H, 2501H : "Get address of first number in H-
L pair. Now H-L points to 2501H"
MOV A, M : "Get first operand in accumulator"
INX H : "Increment content of H-L pair. Now, H-
L points 2502H"
ADD M : "Add first and second operand"
INX H : "H-L points 4002H"
MOV M, A : "Store result at 2503H"
HLT : "Stop"

## Slide 5
5.Subtract two 8-bit numbers
Example
(2501 H) = 49H
(2502 H) = 32H
Result (2503 H) = 49H - 32H = 17H

## Slide 6
LXI H, 2501H : "Get address of first number in H-
L pair. Now H-L Points to 2501H"
MOV A, M : "Get first operand in accumulator"
INX H : "Increment content of H-
L pair. Now, H-L points 2502H"
SUB M : "Subtract first to second operand"
INX H : "H-L points 4002H"
MOV M, A : "Store result at 2503H"
HLT : "Stop"

## Slide 7: Block data transfer 10 bytes from 2200H to 2300H
• MVI C, 0AH ; Initialize counter C= 10
• LXI H, 2200H ; Initialize source memory pointer Data Starts from
2200 location
• LXI D, 2300H ; Initialize destination memory pointer
BK: MOV A, M ; Get byte from source memory block i.e 2200 to
accumulator.
• STAX D ; Store byte in the destination memory block i.e 2300 as
stored in D- E pair
• INX H ; Increment source memory pointer
• INX D ; Increment destination memory pointer
• DCR C ; Decrement counter to keep track of bytes moved
• JNZ BK ; If counter 0 repeat steps
• HLT ; Terminate program

## Slide 8: Problem – Write a program to find the sum of a series where series starts from 3001 memory address and count of series is at 3000 memory address where starting address of the given program is 2000 store result into 4000 memory address.

## Slide 9
Algorithm –
Move 00 to register B immediately for carry
Load the data of memory [3000] into H immediately
Move value of memory into register C
Decrease C by 1
Increase H-L pair by 1
Move value of memory into accumulator
Increase H-L pair by 1
Add value of memory with accumulator
Jump if no carry to step 11
Increase value of register B by one
Decrease register C by 1
Jump if not zero to step-7
Store content of accumulator into memory [4000] (result)
Move content of register B into accumulator
Store content of accumulator into memory [4001] (carry)
Stop

## Slide 10
Memory | Mnemonics | Operands | Comment
2000 | MVI | B, 00 | [B] <- 00
2002 | LXI | H, [3000] | [H-L] <- [3000]
2005 | MOV | C, M | [C] <- [M]
2006 | DCR | C | [C] <- [C] – 1
2007 | INX | H | [H-L] <- [H-L] + 1
2008 | MOV | A, M | [A] <- [M]
2009 | INX | H | [H-L] <- [H-L] + 1
200A | ADD | M | [A] <- [A] + [M]
200B | JNC | 200F | jump if no carry

## Slide 11
Memory | Mnemonics | Operands | Comment
2000 | MVI | B, 00 | [B] <- 00
2002 | LXI | H, [3000] | [H-L] <- [3000]
2005 | MOV | C, M | [C] <- [M]
2006 | DCR | C | [C] <- [C] – 1
2007 | INX | H | [H-L] <- [H-L] + 1
2008 | MOV | A, M | [A] <- [M]
2009 | INX | H | [H-L] <- [H-L] + 1
200A | ADD | M | [A] <- [A] + [M]
200B | JNC | 200F | jump if no carry
200E | INR | B | [B] <- [B] + 1
200F | DCR | C | [C] <- [C] – 1
2010 | JNZ | 2009 | jump if not zero
2013 | STA | [4000] | result
2016 | MOV | A, B | [A] <- [B]
2017 | STA | [4001] | carry
201A | HLT |  | Stop

## Slide 12
6. Add two 16-bits numbers
Add the 16-bit number in memory locations 2501H and 2502H to the 16-bit number in memory locations 2503H and 2504H.
The most significant eight bits of the two numbers to be added are in memory locations 2502H and 4004H.
Store the result in memory locations 2505H and 2506H with the most significant byte in memory location 2506H.
Example
(2501H) = 15H
(2502H) = 1CH
(2503H) = B7H
(2504H) = 5AH
Result = 1C15 + 5AB7H = 76CCH
(2505H) = CCH
(2506H) = 76H

## Slide 13
Program
Add two 16-bits number with ADD and ADC instruction
LHLD 2501H : "Get 1st 16-bit number in H-L pair"
XCHG : "Save 1st 16-bit number in DE"
LHLD 2503H : "Get 2nd 16-bit number in H-L pair"
MOV A, E : "Get lower byte of the 1st number"
ADD L : "Add lower byte of the 2nd number"
MOV L, A : "Store result in L-register"
MOV A, D : "Get higher byte of the 1st number"
ADC H : "Add higher byte of the 2nd number with CARRY"
MOV H, A : "Store result in H-register"
SHLD 4004H : "Store 16bit result in memory locations 2505H and
2506H"
HLT : "Stop"

## Slide 14
7. Add two 16-bits numbers with DAD instruction
LHLD 2501H : "Get 1st 16-bit number"
XCHG : "Save 1st 16-bit number in DE"
LHLD 2503H : "Get 2nd 16-bit number in H-L"
DAD D : "Add DE and HL"
SHLD 2505H : "Store result at locations 2505H
and 2506H
"HLT : "Stop"

## Slide 15
8.Add contents of two memory locations
Example
(2500H) = 7FH
(2501H) = 89H
Result = 7FH + 89H = lO8H
(2502H) = 08H
(2503H) = 01H

## Slide 16
Program
LXI H, 2500H : "HL Points 2500H"
MOV A, M : "Get first operand"
INX H : "HL Points 2501H"
ADD M : "Add second operand"
INX H : "HL Points 2502H"
MOV M, A : "Store the lower byte of result at 2502H"
MVIA, 00 : "Initialize higher byte result with 00H"
ADC A : "Add carry in the high byte result"
INX H : "HL Points 2503H"
MOV M, A : "Store the higher byte of result at 2503H"
HLT : "Terminate program execution"

## Slide 17
9. Finding 1's complement of a number
To obtain one's complement of a number its 0 bits are replaced by 1 and 1 by 0.
Example 1
(2501H) = 96 H = 1001 0110
(9) (6)
One's complement = 0110 1001 = 69 H
Result = (2502H) = 69H
Example 2
(2501H) = E4H
Result = (2502H) = 1BH

## Slide 18
Program
The number is placed in the memory location 2501 H.
The result is stored in the memory location 2502 H.
LDA 2501H : "Get the number IN accumulator"
CMA : "take its complement"
STA 2502H : "Store result in 2502H"
HLT : "Stop"

## Slide 19
10.Finding 2's complement of a number
2's complement of a number is obtained by adding 1 to the 1's complement of the number.
Example
To find the two's complement of 96.
96 = 1001 0110
1's complement = 0110 1001 = 69
+ 0000 0001
2's complement = 0110 1010 = 6A

## Slide 20
Program
The number is placed in the memory location 2501 H.
The result is to be stored in the memory location 2502 H.
LDA 2501 H : "Get data in accumulator"
CMA : "Take its 1's complement"
ADI, 01 H : "Add one in the number"
STA 2502 H : "Store the result in 2502 H"
HLT : "Stop"

## Slide 21
11.Count number of 1's in a number

## Slide 22
Program
Count number of 1's of the content of the register D and store the count in the register B.
MVI B, 00H
MVI C, 08H
MOV A, D
BACK: RAR
JNC SKIP
INR B
SKIP: DCR C
JNZ BACK
HLT

## Slide 23
12.Find larger of two numbers
Example
2501H = 98 H
2502H = 87H
Result = 98H (2503H)

## Slide 24
Program
The first number 98H is placed in the memory location 2501 H. The second number 87H is placed in the memory location 2502H. The result is stored in the memory location 2503 H.
LXI H, 2501H : "Address of first number in H-L pair"
MOV A, M : "1stt number in accumulator"
INX H : "Address of 2nd number in H-L pair"
CMP M : "compare 2nd number with 1st number"
JNC AHEAD : "No, larger is in accumulator. Go to AHEAD"
MOV A, M : "Yes, get 2nd number in the accumulator"
AHEAD :STA 2503 H : "Store larger number in 2503H"

## Slide 25
13.Calculate the sum of series of even numbers
Example
2500 H = 4H
2501 H = 20H
2502 H = 15H
2503 H = 13H
2504 H = 22H
Result = 2505 H = 20+22= 42H

## Slide 26: 14.Program The numbers are placed in the memory locations 2501 to 2504H. The sum is to be stored in the memory location 2450H. As there are 4 numbers in the series, count = 04 The initial value of the sum is made 00. The even number of the series are taken one by one and added to the sum.

## Slide 27
LDA 2500H Load A with count valaue
MOV C, A : "Initialize counter"
MVI B, 00H : "sum = 0"
LXI H, 2501H : "Initialize pointer"
BACK: MOV A, M : "Get the number"
ANI 01H : "Mask Bit l to Bit7"
JNZ SKIP : "Don't add if number is ODD"
MOV A, B : "Get the sum"
ADD M : "SUM = SUM + data"
MOV B, A : "Store result in B register"
SKIP: INX H : "increment pointer"
DCR C : "Decrement counter"
JNZ BACK : "if counter 0 repeat"
STA 2505H : "store sum"
HLT : "Stop"

## Slide 28
15.Calculate the sum of series of odd numbers
Example
2500 H = 4H
2501 H = 9AH
2502 H = 52H
2503 H = 89H
2504 H = 3FH
Result = 2505 H = 89H + 3FH= C8H
Program
The numbers are placed in the memory locations 2501 to 2504H.
The sum is to be stored in the memory location 2450H.
As there are 4 numbers in the series, count = 04
The initial value of the sum is made 00. The odd number of the series are taken one by one and added to the sum

## Slide 29
LDA 2500H
MOV C, A : "Initialize counter"
LXI H, 2501H : "Initialize pointer"
MVI E, 00 : "Sum low = 0"
MOV D, E : "Sum high = 0"
BACK: MOV A, M : "Get the number"
ANI 01H : "Mask Bit 1 to Bit-7"
JZ SKIP : "Don't add if number is even"
MOV A, E : "Get the lower byte of sum"
ADD M : "Sum = sum + data"
MOV E, A : "Store result in E register"
JNC SKIP
INR D : "Add carry to MSB of SUM"
SKIP: INX H : "Increment pointer"

## Slide 30
16.Find the square of given number
Program
Find the square of 07 (decimal) using lookup table techniques.
The number 07 D is in the memory.
The result is to be stored in the memory location 2501H.
The table for square is stored from 2600 to 2609 H.

## Slide 31
LDA 2500H : "Get data in accumulator"
MOV L, A : "Get data in register L"
MVI H, 26H : "Get 26 in register H"
MOV A, M : "Square of data in accumulator"
STA 2501 H : "Store Square in 2501 H"
HLT : "Stop"

## Slide 32
17.Separate even numbers from given numbers
Program
Let's see the program to separate even numbers from the given list of 50 numbers and store them in other location starting from 2600H.
Starting location of 50 number list is 2500H

## Slide 33
LXI H, 2500H : "Initialize memory pointer 1"
LXI D, 2600H : "Initialize memory pointer2"
MVI C, 32H : "Initialize counter"
BACK:MOV A, M : "Get the number"
ANI 01H : "Check for even number"
JNZ SKIP : "If ODD, don't store"
MOV A, M : "Get the number"
STAX D : "Store the number in result list"
INX D : "Increment pointer 2"
SKIP: INX H : "Increment pointer 1"
DCR C : "Decrement counter"
JNZ BACK : "If not zero, repeat"
HLT : "Stop"

## Slide 35: Add two 16-bit numbers
Source Program 1:
LHLD 4000H : "Get first I6-bit number in HL"
XCHG : "Save first I6-bit number in DE"
LHLD 4002H : "Get second I6-bit number in HL"
MOV A, E : "Get lower byte of the first number"
ADD L : "Add lower byte of the second number"
MOV L, A : "Store result in L register"
MOV A, D : "Get higher byte of the first number"
ADC H : "Add higher byte of the second number with CARRY"
MOV H, A : "Store result in H register"
SHLD 4004H : "Store I6-bit result in memory locations 4004H and 4005H"
HLT : "Terminate program execution"

## Slide 36
Source program 2:
LHLD 4000H : Get first I6-bit number
XCHG : Save first I6-bit number in DE
LHLD 4002H : Get second I6-bit number in HL
DAD D : Add DE and HL
SHLD 4004H : Store I6-bit result in memory locations 4004H and 4005H.
HLT : Terminate program execution

## Slide 37
Add the contents of memory locations 40001H and 4001H and place the result in the memory locations 4002Hand 4003H.
(4000H) = 7FH
(400lH) = 89H
Result = 7FH + 89H = lO8H
(4002H) = 08H
(4003H) = 0lH

## Slide 38
Source program:
LXI H, 4000H : "HL Points 4000H"
MOV A, M : "Get first operand"
INX H : "HL Points 4001H"
ADD M : "Add second operand"
INX H : "HL Points 4002H"
MOV M, A : "Store the lower byte of result at 4002H"
MVIA, 00 : "Initialize higher byte result with 00H"
ADC A : "Add carry in the high byte result"
INX H : "HL Points 4003H"
MOV M, A : "Store the higher byte of result at 4003H"
HLT : "Terminate program execution"

## Slide 39
Find the l’s complement of the number stored at memory location 4400H and store the complemented number at me
mory location 4300H.
Sample problem:
(4400H) = 55H
Result = (4300B) = AAB

## Slide 40
LDA 4400B : "Get the number"
CMA : "Complement number"
STA 4300H : "Store the result"
HLT : "Terminate program execution"

## Slide 41
Find the 2′s complement of the number stored at memory location 4200H and store the complemented number at memory location 4300HSample problem:
(4200H) = 55H
Result = (4300H) = AAH + 1 = ABH

## Slide 42
Source program:
LDA 4200H : "Get the number"
CMA : "Complement the number"
ADI, 01 H : "Add one in the number"
STA 4300H : "Store the result"
HLT : "Terminate program execution"

## Slide 43: ADDITION OF TWO 8 BIT NUMBERS
AIM: To perform addition of two 8 bit numbers using 8085.
ALGORITHM:
Start the program by loading the first data into Accumulator.
Move the data to a register (B register).
Get the second data and load into Accumulator.
Add the two register contents.
Check for carry.
Store the value of sum and carry in memory location.
Terminate the program.

## Slide 44
Input: | 80 (4150)
 | 80 (4251)
Output: | 00 (4152)
 | 01 (4153)

## Slide 45
MVI | C, 00 | Initialize C register to 00
LDA | 4150 | Load the value to Accumulator.
MOV | B, A | Move the content of Accumulator to B register.
LDA | 4151 | Load the value to Accumulator.
ADD | B | Add the value of register B to A
JNC | LOOP | Jump on no carry.
INR | C | Increment value of register C
LOOP: STA | 4152 | Store the value of Accumulator (SUM).
MOV | A, C | Move content of register C to Acc.
STA | 4153 | Store the value of Accumulator (CARRY)
HLT |  | Halt the program.
PROGRAM:

## Slide 46
Source program:
LXI H, 4000H : "HL Points 4000H"
MOV A, M : "Get first operand"
INX H : "HL Points 4001H"
ADD M : "Add second operand"
INX H : "HL Points 4002H"
MOV M, A : "Store the lower byte of result at 4002H"
MVIA, 00 : "Initialize higher byte result with 00H"
ADC A : "Add carry in the high byte result"
INX H : "HL Points 4003H"
MOV M, A : "Store the higher byte of result at 4003H"
HLT : "Terminate program execution"

## Slide 47
Search the given byte in the list of 50 numbers stored in the consecutive memory locations and store the address of memory location in the memory locations 2200H and 2201H.
Assume byte is in the C register and starting address of the list is 2000H. If byte is not found store 00 at 2200H and 2201H.

## Slide 48
LX I H, 2000H :"Initialize memory pointer 52H"
MVI B, 52H :"Initialize counter"
BACK: MOV A, M :"Get the number"
CMP C :"Compare with the given byte"
JZ LAST :"Go last if match occurs"
INX H :"Increment memory pointer"
DCR B :"Decrement counter"
JNZ B :"If not zero, repeat"
LXI H, 0000H
SHLD 2200H
JMP END :"Store 00 at 2200H and 2201H"
LAST: SHLD 2200H :"Store memory address"
END: HLT :"Stop"

## Slide 49
Find the square of the given numbers from memory location 6100H and store the result from memory location 7000H.Sample problem 2200H = 4H 2201H= 9AH 2202H= 52H 2203H= 89H 2204H= 3FH Result = 89H + 3FH = C8H 2300H= H Lower byte 2301H = H Higher byte

## Slide 50
LXI H, 6200H :"Initialize lookup table pointer"
LXI D, 6100H :"Initialize source memory pointer"
LXI B, 7000H :"Initialize destination memory pointer"
BACK: LDAX D :"Get the number"
MOV L, A :"A point to the square"
MOV A, M :"Get the square"
STAX B :"Store the result at destination memory location"
INX D :"Increment source memory pointer"
INX B :"Increment destination memory pointer"
MOV A, C
CPI 05H :"Check for last number"
JNZ BACK :"If not repeat"
HLT

## Slide 51
Calculate the sum of series of even numbers
Calculate the sum of series of even numbers from the list of numbers. The length of the list is in memory location 2200H and the series itself begins from memory location 2201H. Assume the sum to be 8 bit number so you can ignore carries and store the sum at memory location 2210H.Sample problem 2200H= 4H 2201H= 20H 2202H= l5H 2203H= l3H 2204H= 22H Result 22l0H= 20 + 22 = 42H = 42H

## Slide 52
LDA 2200H
MOV C, A :"Initialize counter"
MVI B, 00H :"sum = 0"
LXI H, 2201H :"Initialize pointer"
BACK: MOV A, M :"Get the number"
ANI 0lH :"Mask Bit l to Bit7"
JNZ SKIP :"Don’t add if number is ODD"
MOV A, B :"Get the sum"
ADD M :"SUM = SUM + data"
MOV B, A :"Store result in B register"
SKIP: INX H :"increment pointer"
DCR C :"Decrement counter"
JNZ BACK :"if counter 0 repeat"
STA 2210H :"store sum"
HLT