## Slide 1: Counters & Time Delays
COUNTERS - Are used to keep track of events.
TIME DELAYS -Accurate timing between two events.

## Slide 2: COUNTERS
A Counter is designed simply
by loading an appropriate
number into one of the
registers and using the INR
DCR (Decrement by
loop
instructions. A established to
update
(Increment by one) or the
one)
is the
count, and each
count is
checked to determine whether
it has reached the final
number; if not, the loop is repeated.
Initialize
Update
Display
Is this Final Count?
Yes
No
Flowchart of a Counter

## Slide 3: TIME DELAYS
The procedure used to design a specific delay is similar to that used to set up a counter.
A register is loaded with a number, depending on the time delay required, and then the register is decremented until it reaches zero by setting up a loop with a conditional jump instruction.
The loop causes the delay, depending upon the clock period of the system.
Load Delay Register
Body of loop
Is this Final Count?
No
Yes
Flowchart of a Time Delay

## Slide 4: Calculating Time Delays
Each instruction combinations of
passes through different Opcode Fetch, Memory Read,
and Memory Write cycles.
Knowing the combinations of cycles, one can calculate how long such an instruction would require to complete.
  Number of Bytes
  Number of Machine Cycles
  Number of T-State.

## Slide 5: Calculating Time Delays
Time Delay = No. of T-States * Clock Period
For example,
“MVI” instruction uses 7 T-States.
Therefore, if the Microprocessor is running at 2 MHz, the instruction would require 3.5 S to complete.
7X(1/(2X106))=3.5 µsec

## Slide 6: Time Delay using following three Techniques:
Using One Register.
Using a Register Pair.
Using a Loop with in a Loop

## Slide 7: Using One Register
A count is loaded in a register, and loop can be used to produce a certain amount of time delay in a program.
The following is an example of a delay using One Register:
 | MVI C, FFH | 7 T-States
LOOP | DCR C | 4 T-States
 | JNZ LOOP | 10 T-States
The first instruction initializes the loop counter and is executed only
once requiring only 7 T-States.
The following two instructions form a loop that requires 14 T-States to execute and is repeated 255 times until C becomes 0.

## Slide 8: Using One Register
We need to keep in mind though that in the last iteration of the loop, the JNZ instruction will fail and require only 7 T-States rather than the 10.
Therefore, we must deduct 3 T-States from the total delay to get an accurate delay calculation.
To calculate the delay, we use the following formula:
Tdelay = TO + TL
Tdelay = total delay
TO = delay outside the loop TL = delay of the loop
TO is the sum of all delays outside the loop.
TL is calculated using the formula
TL = T * Loop T-States * N (no. of iterations)

## Slide 9: Using One Register
Using these formulas, we can calculate the time delay for the previous example:
TO = 7 T-States
(Delay of the MVI instruction)
TL = (14 X 255) - 3 = 3567 T-States
(14 T-States for the 2 instructions repeated 255 times (FF16 = 25510) reduced by the 3 T-States for the final JNZ.)

Tdelay
= [(TO + TL )/f]
= (7 + 3567)/2MHz
= (3574) X 0.5 Sec
= 1.787 mSec
(Assuming f = 2 MHz)

## Slide 10: Using a Register Pair
Using a single register, one can repeat a loop for a maximum count of 255 times.
It is possible to increase this count by using a register pair for the loop counter instead of the single register.
  A minor problem arises in how to test for the final count since DCX and INX do not modify the flags.
  However, if the loop is looking for when the count becomes zero, we can use a small trick by ORing the two registers in the pair and then checking the zero flag.

## Slide 11: Using a Register Pair
The following is an example of a delay loop set up with a register pair as the loop counter.
LOOP
LXI B, 1000H DCX B
MOV A, C ORA B JNZ LOOP
10 T-States
6 T-States
4 T-States
4 T-States
10 T-States

## Slide 12: Using a Register Pair
Using the same formula from before, we can calculate:
TO = 10 T-States
(The delay for the LXI instruction)
TL = (24 X 4096) - 3 = 98301 T- States
(24 T-States for the 4 instructions in the loop repeated 4096 times (100016 = 409610) reduced by the 3 T-States for the JNZ in the last iteration.)
TDelay = (10 + 98301) X 0.5 mSec = 49.155 mSec

## Slide 13: Using a Loop with in a Loop
Nested loops can be
easily setup in
Assembly language by
using two registers for the two loop counters and updating the right register in the right loop.
Initialize loop 1
Update the count1
Is this Final Count?
Body of loop 1
No
Initialize loop 2
Body of loop 2
Yes
Update the count 2
No
Is this Final Count?
Yes
Flowchart for time delay with two loops

## Slide 14: Using a Loop with in a Loop
Instead (or in conjunction with) Register Pairs, a nested loop structure can be used to increase the total delay produced.
 | MVI B, 10H | 7 T-States
LOOP2 | MVI C, FFH | 7 T-States
LOOP1 | DCR C | 4 T-States
 | JNZ LOOP1 | 10 T-States
 | DCR B | 4 T-States
 | JNZ LOOP2 | 10 T-States

## Slide 15: Using a Loop with in a Loop
The calculation remains the same except that the formula must be applied recursively to each loop.
Start with the inner loop, then plug that delay in the calculation of the outer loop.
Delay of inner loop,
TO1 = 7 T-States
(MVI C, FFH instruction)
TL1 = (255 X 14) - 3 = 3567 T-States
(14 T-States for the DCR C and JNZ instructions repeated 255 times (FF16 = 25510) minus 3 for the final JNZ.)
TLOOP1 = 7 + 3567 = 3574 T-States

## Slide 16: Using a Loop with in a Loop
Delay of outer loop
TO2 = 7 T-States
(MVI B, 10H instruction)
TL1 = (16 X (14 + 3574)) - 3 = 57405 T-States
(14 T-States for the DCR B and JNZ instructions and 3574
T-States for loop1 repeated 16 times (1016 = 1610) minus 3 for the final JNZ.)
TDelay = 7 + 57405 = 57412 T-States
Total Delay
TDelay = 57412 X 0.5 Sec = 28.706 mSec

## Slide 17: Increasing the Time Delay
The Delay can be further increased by using register pairs for each of the loop counters in the nested loops setup.
It can also be increased by adding dummy instructions (like NOP) in the body of the loop.

## Slide 18: Counter Design with Time Delay
Display
Update Count
Is Count
Complete?
Time Delay
No
Yes
Initialize Counter
Load Delay Register
Is this Final Count?
Body of loop
No
Yes

## Slide 19
Initialize Counter
Update Count
Display Count
Yes
Is
Count
Complete?
No
Go back
End
Display
Update Count
Time Delay
Is
No Count Complete?
Yes
Initialize Counter
End
Time Delay
Variations Of Counter Flowchart

## Slide 20: Hexadecimal counter
W r it e a p r o g r a m t o co u n t con tinuously
in hexa decimal from FF h to 00 h in a
System w it h a 0 . 5 m icro sec clock period. Use register c to set up a o ne
M illisecond delay between each count and display the numbers a t o ne o f the output ports.

## Slide 21: Hexadecimal counter
This problem has two parts; the first is to set up a continuous down-counter, and the second is to design a given delay between two counts.
  The hexadecimal counter is set up by loading a register with an appropriate starting number and decrementing it until it becomes zero. After zero count, the register goes back to FF because decrementing zero results in a (-1), which is FF in 2’s complement.
  The 1 ms delay between each count is set up by using delay techniques.

## Slide 22: Hexadecimal counter
  20:
2000MVI B,00H
02 DCR B
2003 CALL 2060/DELAY
2006 MOV A,B
2007 OUT PORT# 2009 JMP 2002
2060 MVI C 10
2062 DCR C
2063 JNZ 2062
2066 RET

## Slide 23: Time Delay Calculation
Delay loop includes two instructions: DCR C and JNZ with 14 T-states. Therefore the time delay TL in the loop (without accounting for the fact that JNZ requires 7 T-States in the last cycle, because count will remain same even if the calculations take into account the difference of 3 T-States) is:
TL = 14 T-states X T (Clock period) X Count
= 14 X (0.5 x 10-6) x Count
= (7.0 X 10-6) X Count

## Slide 24
The Delay outside the loop includes the following instructions:
Delay outside the loop:
DCR B
MVI C,COUNT MOV A,B
4T
7T
4T
10T
To = 35 T-States * T
= 35 * (0.5* 10-6)
= 17.5 µs
OUT PORT JMP
10T
35 T-States
Total Time Delay TD = To + TL
1ms= 17.5 * 10-6 + (7.0 *10-6) *Count
Count= 1x 10-3 – 17.5 x 10-6 ≈14010 ==1ms
7.0 x 10-6
Hence, a delay count 8CH(14010) must be loaded in C.

## Slide 29
Using 16-bit register-pair as counter generate a delay of 0.5 second

## Slide 30
10 + (6 + 4 + 4 + 10) * 65535H – 3 + 10 = 17 + 24 * 65535H = 1572857. So the time delay will be 1572857 * 1/3µs = 0.52428s. Here we are getting nearly 0.5s delay.