## Slide 1: Topics
Demultiplexing of buses
Generation of control signals
Instruction Set

## Slide 2
The address bus has 8 signal lines A8 – A15 which are unidirectional.
The other 8 address bits are multiplexed(time shared) with the 8 data bits.
AD0 –AD7 are bi-directional and serve as A0 –A7and D0 –D7 at the same time.
During the execution of the instruction, these lines carry the address bits during the early part, then during the later part of the execution, they carry the 8 data bits.
In order to separate the address from the data, we can use a latch to save the value before the function of the bits changes.

## Slide 3: Demultiplexing of AD7-AD0
The high order bits of the address remain on the bus for three clock periods.
However, the low order bits remain for only one clock period and they would be lost if they are not saved externally.

## Slide 4
To make sure we have the entire address for the full three clock cycles, an external latch to save the value of AD7–AD0 when it is carrying the address bits.
We use the ALE signal to enable this latch.
ALE operates as a pulse during T1 to latch the address. Then when ALE goes low, the address is saved and the AD7–AD0 lines can be used for their purpose as the bi-directional data lines D0 to D7.

## Slide 5
Opcode fetch cycle timing diagram

## Slide 7: Generation of Control signal

## Slide 8: Truth Table of Status Signal

## Slide 9: INSTRUCTION SET OF 8085

## Slide 10: Instruction Set of 8085
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions .
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or
Instruction Byte.

## Slide 11: Classification of Instruction Set
Data Transfer Instruction
Arithmetic Instructions
Logical Instructions
Branching Instructions
Machine Control Instructions

## Slide 12: 1.Data Transfer Instructions
These instructions move data between registers, or between memory and registers.
These instructions copy data from source to destination(without changing the original data ).

## Slide 13: DATA TRANSFER (COPY) OPERATIONS
Load a 8-bit number in a Register
Copy from Register to Register
Copy between Register and Memory
Copy between Input/Output Port and Accumulator
Load a 16-bit number in a Register pair
Copy between Register pair and Stack memory

## Slide 14: MOV-Copy from source to destination
Opcode Operand
MOV
Rd, Rs M, Rs Rd, M
This instruction copies the contents of the source register into the destination register. (contents of the source register are not altered)
If one of the operands is a memory location, its location is specified by the contents of the HL registers.
Example: MOV B, C or MOV B, M

## Slide 15
A 20 B
20
A |  | F | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A | 20 | B | 
BEFORE EXECUTION
AFTER EXECUTION
MOV B,A
A |  | F | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A F |  |  | 
B |  | C | 
D |  | E | 
H | 20 | L | 50
A F |  |  | 
B |  | C | 40
D |  | E | 
H | 20 | L | 50
MOV M,B
MOV C,M
40
40
30

## Slide 16: MVI-Move immediate 8-bit
Opcode Operand
MVI
Rd, Data M, Data
The 8-bit data is stored in the destination register or memory.
If the operand is a memory location, its location is specified by the contents of the H-L registers.
Example: MVI B, 60H or MVI M, 40H

## Slide 17: BEFORE EXECUTION
A F |  | 
B |  | C
D E |  | 
H L |  | 
A F |  | 
B | 60 | C
D E |  | 
H L |  | 
AFTER EXECUTION
MVI B,60H
40
HL=2050
2051H
204FH
204F
2051H
MVI M,40H
BEFORE EXECUTION
AFTER EXECUTION
HL=2050

## Slide 18: Write an assembly language program to add two 8 bit numbers
ADDRESS | OPCODE | MNEMONIC | OPERAND | COMMENTS
C000 | 3E Data1 | MVI | A, Data1 | Get first byte in the accumulator
C002 | 06 Data2 | MVI | B, Data2 | Get Second byte in register B
C004 | 88 | ADD | B | Addition of Data1 (A) + Data2 (B). Result is saved in accumulator A.
C005 | 76 | HLT (RST 1) |  | Halt/end the program

## Slide 19: LDA-Load accumulator
Opcode
Operand
LDA
16-bit address
The contents of a memory location, specified by a 16- bit address in the operand, are copied to the accumulator.
The contents of the source are not altered.
Example: LDA 2000H

## Slide 20
A
30
A
30
30
AFTER EXECUTION
BEFORE EXECUTION
LDA 2000H
2000H
2000H

## Slide 21: LDAX-Load accumulator indirect
Opcode Operand
LDAX
B/D Register Pair
The contents of the designated register pair point to a memory location.
This instruction copies the contents of that memory location into the accumulator.
The contents of either the register pair or the memory location are not altered.
Example: LDAX D

## Slide 22: AFTER EXECUTION
A
F
B
C
D 20 E 30
A
80
F
B
C
D 20 E 30
80
80
BEFORE EXECUTION
LDAX D
2030H
2030H

## Slide 23: LXI-Load register pair immediate
Opcode Operand
LXI
Reg. pair, 16-bit data
This instruction loads 16-bit data in the register pair.
Example: LXI H, 2030 H

## Slide 24
A
F
B
C
H L
A | 80 | F | 
B |  | C | 
H | 20 | L | 30
50
90
50
AFTER EXECUTION
BEFORE EXECUTION
LXI H, 2030
2030H
2030H
2031H
M=50

## Slide 25: LHLD-Load H and L registers direct
Opcode Operand
LHLD
16-bit address
This instruction copies the contents of memory location pointed out by 16-bit address into register L.
It copies the contents of next memory location into register H.
Example: LHLD 2030 H

## Slide 26
A
F
B
C
H L
A | 80 | F | 
B |  | C | 
H | 85 | L | 00
00
85
60
AFTER EXECUTION
BEFORE EXECUTION
LHLD 2030
2030H
8500H
M=60

## Slide 27: (COPY) OPERATIONS INSTRUCTIONS
/
Load a 8-bit number 4F in register B
Copy from Register B to Register A
Load a 16-bit number 2050 in Register pair HL
Copy from Register B to Memory Address 2050
Copy between Input/Output Port and Accumulator
MVI B, 4FH
MOV A,B
LXI H, 2050H
MOV M,B
OUT 01H
IN 07H