## Slide 1: MICROCONTROLLER-8051

## Slide 3: Overview
Introduction
Block Diagram and Pin Description of the 8051
Registers
Memory mapping in 8051 Stack in the 8051
I/O Port Programming
Timers
Interrupts & Applications

## Slide 4: Why do we need to learn Microcontrollers ?
Today there is no electronic gadget on the earth which is designed without a Microcontroller. Ex: communication devices, digital entertainment, portable devices etc…

## Slide 5
Personal information products: Cell phone, pager, watch, pocket recorder, calculator
Laptop components: mouse, keyboard, modem, fax card, sound card, battery charger
Home appliances: door lock, alarm clock, thermostat, air conditioner, TV remote, VCR, small refrigerator, exercise equipment, washer/dryer, microwave oven
Industrial equipment: Temperature/pressure controllers, Counters, timers, RPM Controllers
Toys: video games, cars, dolls, etc.

## Slide 6: Then What is a Microcontroller ?
CPU | RAM | ROM
I/O Port | Timer | Serial COM Port
A smaller computer
On-chip RAM, ROM, I/O ports...
Example ： Motorola’s 6811, Intel’s 8051, Zilog’s Z8 and PIC 16X
A single chip Microcontroller

## Slide 7: How is it different from a Microprocessor ??
General-purpose microprocessor
CPU for Computers
No RAM, ROM, I/O on CPU chip itself Example ： Intel’s x86, Motorola’s 680x0
CPU
General- Purpose Micro- processor
RAM
ROM
I/O
Port
Timer
Serial COM
Port
Data Bus
Address Bus

## Slide 8: Microprocessor vs. Microcontroller
Microprocessor
CPU is stand-alone, RAM, ROM, I/O, timer are separate



designer can decide on the amount of ROM, RAM and I/ O ports.
expansive versatility general-purpose
Microcontroller
CPU, RAM, ROM, I/O and timer are all on a single chip
fix amount of on-chip ROM, RAM, I/O ports
Highly bit addressable
for applications in which cost, power and space are critical
single-purpose

## Slide 9: ARM Controllers
In recent times ARM company (Advanced Risc machines) has developed and introduced 32 bit controllers which are highend application devices,especially communication devices like mobiles , ipods etc..(Refer www.arm.com)

## Slide 10: Types of Microcontrollers

## Slide 11: MCS-51 “Family” of Microcontollers
Feature
ROM
8031 8051 8052 8751
NO 4kB 8kB 4kB UV Eprom
RAM (Bytes) 128
128
256
128
TIMERS
2
2
3
2
I/O PINS
32
32
32
32
SERIAL PORTS 1
1
1
1
6
6
8
6
INTERRUPT SOURCES

## Slide 12: Microcontroller Architectures
CPU
Program
+ Data
Data Bus
Von Neumann
Architecture
CPU
Program
Address Bus
Data Bus
Harvard
Architecture
Memory
Data
Address Bus
Fetch Bus
Memory
Address Bus 0
0
0
2n

## Slide 13
In Harvard architecture, the CPU is connected with both the data memory (RAM) and program memory (ROM), separately.
In Von-Neumann architecture, there is no separate data and program memory.
Instead, a single memory connection is given to the CPU. ...
Von-Neumann Architecture requires less space.

## Slide 14: Important Features of 8051
4K bytes ROM
128 bytes RAM
Four 8-bit I/O ports
Two 16-bit timers
Serial interface
64K external code memory space
64K data memory space

## Slide 15: “Original” 8051 Microcontroller
Oscillator and timing
4096 Bytes Program Memory (ROM)
128 Bytes Data Memory (RAM)
Two 16 Bit Timer/Event Counters
8051
CPU
64 K Byte Bus Expansion Control
Programmable I/ O
Programmable Serial Port Full Duplex UART Synchronous Shifter
Internal data bus
External interrupts
subsystem interrupts
Control
Parallel ports
Address Data Bus
I/O pins
Serial Input
Serial Output